## Slide 1
Dialysis Adequacy
พ. เจริญ เกียรติวัชรชัย
21 พค 2568: 16:00 น

## Slide 2
We recommend that patients on HD must receive 3 times dialysis in a week for at least 4 h each time with BF of 300 ml/min and DF of 500 ml/min
Recommendation :

## Slide 3
นิยาม & การประเมิน adequacy
ความสัมพันธ์ Kt/V & URR
Single-pool vs double pool Kt/V
การปรับ dialysis prescription เพื่อเพิ่ม Kt/V
ปัญหาและการพัฒนาหน่วยงาน
เนื้อหา :

## Slide 4
Adequacy of dialysis refers to how well we remove toxins and waste products from the patient’s blood, and has a major impact on their well-being
นิยาม:

## Slide 5
Evolution of the concept of dialysis adequacy.:

## Slide 6
Kt/Vurea : NOT THE SAME

## Slide 7
Combined assessment of
  laboratory markers
  overall clinical status
should be taken into consideration in the determination of adequacy and adjustment of the dialysis prescription
Dialysis Adequacy:
Indian Journal of Nephrology 2021

## Slide 8
small molecules (prototype: urea, and Kt/V)**
middle molecules (prototype: 2-microglobulin)
clinical and nutritional markers (prototype : albumin)
Three main markers of dialysis adequacy:

## Slide 9: Common Measures of Adequacy
Urea Reduction Ratio (URR)
Kt/Vurea
  single pool  spKt/V
  equilibrated (Double pool)  eqKt/V
  etc

## Slide 10
Urea was the first identified marker of kidney function, hence the name uremic syndrome.
Later, creatinine took over in the evaluation of kidney function but urea resurged as a marker of dialysis efficiency
Urea

## Slide 11
The URR was first popularized by Lowrie and Lew in 1991
URR of > 65% is recommended as a marker of adequacy for patients who are stable on HD 3 times / wk
URR closely related to Kt/V : spKt/V = -ln (1-URR)
Urea reduction ratio (URR)
Indian Journal of Nephrology 2021

## Slide 12
Pt A : BWPre 70kg, BUNPre 80 , BUNPost 40 mg/dl, UF 3 L
Pt B : Same but UF 0 L
Pt A : urea loss  36 – 16.8 = 19.2 gm
  VPre 45 L  urea = 0.8 x 45 = 36 gm
  VPost 42 L -- > urea 0.4 x 42 = 16.8 gm
Pt B : urea loss  36 – 18 = 18 gm
  VPost 45 L -- > urea 0.4 x 45 = 18 gm
URR : limitation
Indian Journal of Nephrology 2021

## Slide 13
Nomogram relating Kt/V and URR
Notes: วิธีการใช้งานโนโมแกรมเริ่มต้นที่แกนแนวตั้ง: หาค่า URR ที่ได้จากการวัดก่อนและหลังการฟอกไต​เลื่อนตามแนวนอน: ไปยังเส้นโค้งที่ตรงกับค่า UF/W ของผู้ป่วย (เช่น ถ้าน้ำหนักลดลง 2 กก. จากน้ำหนักหลังฟอกไต 70 กก. จะได้ UF/W = 0.0286 หรือประมาณ 2.86%)​อ่านค่าจากแกนนอน: ค่าที่ได้คือค่า Kt/V ที่ประมาณจากโนโมแกรม​โนโมแกรมนี้มีประโยชน์ในการประเมินประสิทธิภาพของการฟอกไต โดยไม่ต้องคำนวณค่า Kt/V ด้วยสูตรที่ซับซ้อน อย่างไรก็ตาม ควรใช้ร่วมกับการประเมินทางคลินิกอื่น ๆ เพื่อให้ได้ข้อมูลที่ครบถ้วนและแม่นยำ

## Slide 14
the National Cooperative Dialysis Study (NCDS)
developed in the 1980 after it was shown that the blood urea level influenced survival in adult patients
Kt/Vurea: concept
Pediatric Nephrology (2019)

## Slide 15
Developed by Frank Gotch and John Sargent in 1985
K : dialyzer urea clearance,
t : total dialysis session time
V : volume of distribution of urea, TBW
Kt/Vurea:
Frank Gotch

## Slide 16
single pool Kt/V (spKt/V)**
double pool Kt/V (equilibrated)*
estimated weekly Kt/V
standard Kt/V
BSA normalized standard Kt/V.
Kt/Vurea: calculation
Indian Journal of Nephrology 2021
Notes: Single pool Kt/V is most commonly measured parameter
for measuring dialysis adequacy. Double pool Kt/V is more
accurate but needs the patient to wait for 30‑60 minutes
post dialysis.

## Slide 17
assumed urea is in only one compartment of the body and that there is a linear decline in urea level during HD, and an immediate equilibration occurs between the IC and EC compartments after HD.
spKt/Vurea : non‑equilibrated
Indian Journal of Nephrology 2021
Notes: Single pool Kt/V is most commonly measured parameter
for measuring dialysis adequacy. Double pool Kt/V is more
accurate but needs the patient to wait for 30‑60 minutes
post dialysis.

## Slide 18
spKt/V = [‑ ln (R – 0.008 x T)] + [(4 – 3.5 x R) x 0.55 x UFV/V]
R : ratio of BUNpost to BUNpre
T : dialysis session time in hours
UFV : ultrafiltration volume
V : TBW volume in L
spKt/Vurea: formula
Indian Journal of Nephrology 2021
Notes: Equation 1 for calculating spKt/V does not give accurate
results when hemodialysis sessions are fewer than 3 times
per week (or more ‑ up to 7 times per week) due to
differences in inter dialytic urea generation.

## Slide 19
spKt/V = [‑ ln (R – 0.008 x T)] + [(4 – 3.5 x R) x 0.55 x UFV/V]
Notes: Equation 1 for calculating spKt/V does not give accurate
results when hemodialysis sessions are fewer than 3 times
per week (or more ‑ up to 7 times per week) due to
differences in inter dialytic urea generation.

## Slide 20
Kt/Vurea : NOT THE SAME

## Slide 21
spKt/V = ‑ ln (R–GFAC x T) + (4 – 3.5 x R) x 0.55 x UFV/V
GFAC or G‑factor (urea generation factor that adjusts for urea generation) value
spKt/Vurea: formula
Indian Journal of Nephrology 2021
Notes: Equation 1 for calculating spKt/V does not give accurate
results when hemodialysis sessions are fewer than 3 times
per week (or more ‑ up to 7 times per week) due to
differences in inter dialytic urea generation.

## Slide 22
GFAC or G‑factor
Indian Journal of Nephrology 2021

## Slide 24
two compartments of BUN : IC and EC compartments.
If sample is drawn after 30-60 min of stopping dialysis, the rebound gets completed, and we get a more accurate and true BUN-post level.
Double pool Kt/Vurea : equilibrated
Indian Journal of Nephrology 2021
IC
EC

## Slide 25
eKt/Vurea is usually 0.15 to 0.20 < sp-Kt/V.
This difference is due to the ‘rebound’.
eKt/Vurea vs spKt/Vurea :
Indian Journal of Nephrology 2021

## Slide 26
the smallest patients (with smallest ‘V’) will have highest K/V, and highest rebounds.
This means that spKt/V may be higher for small patients, and eqKt/V much lower due to higher rebounds
The magnitude of ‘rebound’:
Indian Journal of Nephrology 2021

## Slide 27
BFR(QB), DFR(QD) and UFR
KoA (mass transfer-area coefficient)
  SA of the membrane, and
  Intrinsic diffusive capacity of the membrane
Clearance of urea: dependent on
Indian Journal of Nephrology 2021

## Slide 28
Estimated (theoretical) dialysis dose (1)
Indian Journal of Nephrology 2021

## Slide 29
Estimated (theoretical) dialysis dose (2)
สมการ simplified resistance-in-series model:

## Slide 30
Urea Clearance vs Blood Flow Rate
K0A = 800 ml/min
QD​ = 500 ml/min

## Slide 31
Urea Clearance vs Blood Flow Rate
K0A = 250 ml/min
QD​ = 500 ml/min

## Slide 32
Urea Clearance vs Dialysate Flow Rate
K0​A = 250 ml/min

## Slide 33
การปรับเพิ่ม Kurea
อันดับ | ปัจจัยที่เพิ่ม | ข้อจำกัด
1 | เพิ่ม K₀A : เปลี่ยน dialyzer ที่มี K₀A สูงกว่า | ต้องเปลี่ยนไส้กรอง, มีค่าใช้จ่าย
2 | เพิ่ม QB: เพิ่ม Q_B ก่อน (จนถึง 300–400 ml/min) | หลอดเลือดผู้ป่วยอาจรับไม่ไหว
3 | เพิ่ม QDเฉพาะช่วงแรก ๆ (เช่น 300 → 500 ml/min) | เฉพาะช่วงแรก ๆ ถ้ามากกว่านั้นมักไม่คุ้ม สิ้นเปลือง dialysate

## Slide 34
ปัญหาและแนวทางพัฒนา:

## Slide 35: THANK YOU